## Slide 1
Propane
Leecher's Propane family business - George & Kevin Leecher George@LechnersPropane.com Kevin@LechnersPropane.com +1(607) 363-2434 • Work
1217 Burnwood Rd, East Branch, NY 13756-2109
https://www.lechnerspropane.com
Price (June 2022): 4.65/gallon
Expect $60 refill every 2 months
Backup Generator
min 12KW
better 20-26KW

## Slide 2
Propane
Tank has pressure 100-200 PSI (up to 250 PSI in hot weather and full tank)
Cooking stove uses 0.4 PSI
The reduction of pressure in two steps: to 10 PSI, then to 0.4 PSI
Tank should be transported only in vertical state
Tank should be filled no more than 80% (to leave some space for expansion)
A full100 lb propane tank weighs ~ 170 lbs. It holds ~23.6 gallons of propane, and propane weighs around 4.2 pounds per gallon.
Measure fulness: by weight, by sound, by temperature,
ultrasound meter - truma propane level check
Line Regulator
(pressure regulator)
To transfer propane from one tank to another one needs specialized propane transfer pump designed for LPG (Liquid Petroleum Gas), proper fittings, hoses and safety valves.
Most common pump type is a sliding vane pump. It has a rotor with sliding vanes that create sealed chambers to move the liquid propane without allowing it to vaporize.