## Slide 1
John Deere 425 (and 445)
1992 - 2001
Built in Horicon, Wisconsin, USA
Original price was $8,995 in 1995
Weight – 805 lbs (365kg)
Engine: 20HP Kawasaki 617cc 2-cyl gasoline
carburetor
(model 445 has 22 hp and fuel injection)
Fuel tank: 6.5 gal (regular gasoline, no ethanol)
Oil - 10W30
Transmission: hydrostatic
Two-wheel drive, differential lock (mechanical rear)
Power Steering
425 Serial Numbers
https://www.tractordata.com/lawn-tractors/000/0/4/43-john-deere-425.html
Year. First tractor
1993 010001
1994 020001
1995 030001 M00425A-036065
1996 040001
1997 050001
1998 060001
1999 070001
2000 080001
2001 090001
Our JD 425 1995
Engine: Kawasaki
Liquid Cooled V-TWIN 20 HP OHV FD620D John Deere K Series
Spark Plugs AM101194 (short)
https://partscatalog.deere.com/jdrc/sidebyside/equipment/73515/referrer/navigation/pgId/2523090
Note: there are two models of spark plugs:
AM101194 (short) for engine marked ASO2, BSO2, CSO2, DSO2, ESO2, FSO2
M805853 (long) for engine marked GSO2
We have the short one
On Amazon:
NGK Spark Plugs BMR4A #5728 (box of 10)
The spark plug wrench socket is 3/4"

## Slide 2
Meg-Mo blades
https://meg-mo.com
The MEG-MO™ Rotary Mulching Blade System
Center hole - round
Current Blade OEM Part # M115495
To order I need to provide this info:
John Deere Standard Mower Blade for 48" deck
Part Number: M115495
Hole in the center – round, 13/16 inch
Length of the blade (rotating diameter) 16 5/8 inch
Nut M18
E-Mail: sales@meg-mo.com Call (877) 625-0125
Received call from 815-625-0125
Searching John Deere Parts:
.. https://partscatalog.deere.com/jdrc/navigation/equipment/73515
Then go to mower deck attachment:
.. https://partscatalog.deere.com/jdrc/navigation/equipment/78976
Then select "20 Mid-Mount Mower Decks 48-Inch and 54-Inch (For 425, 445 and 455 LGT)"
Then select "Belt Drive, Blades, Idlers and Spindles - ST561860"
.. https://partscatalog.deere.com/jdrc/sidebyside/equipment/78976/referrer/navigation/pgId/2341197
The John Deere Blade Bolt - 19M7788 (requires M18 nut driver (18mm)):
.. https://www.greenpartstore.com/John-Deere-Blade-Bolt-19M7788.html
Riding mower blades should be installed between
70 and 90 foot pounds of torque
LEXIVON 1/2-Inch Drive LX-183 (10-150 Ft-lb)
https://www.amazon.com/LEXIVON-2-Inch-Torque-13-6-203-5-LX-183/dp/B07MP1Q3W8/

## Slide 3
JohnDeere 425 Tires
Otar Recommends
TireJect Tire Sealant & Bead Sealer Kit:
https://www.amazon.com/dp/B08WKX95B9/
Tim (dealer) recommends:
LiquiTube tire sealant
front 16 x 7.50 - 8 (2-ply 8-12 PSI)
rear 23 x 10.50 – 12 (2-ply 6-10 PSI)
Tire Pressure from the manual:
Tire Size | Ply Rating | Pressure (PSI)
16 x 7.50 – 8 | 2 | 8-12
18 x 8.50 – 8 | 4 | 6-22
23 x 8.50 – 12 | 2 | 6-10
23 x 10.5 - 12 | 2 | 6-10
26 12.00 - 12 | 2 | 6-10
26 12.00 - 12 | 4 | 6-20
We may need to install Tire Tubes (~$15 each)
Tire "23 x 10.5 – 12":
23" = overall diameter
10.5" = width of the tire 12" = rim diameter

## Slide 4
60" deck, spindles, pulley
deck
spindle hub
with pulley
spindle shaft
bearing
bearing
pulley
spindle shaft
inserted from here
insert
bushing
nut
bushing
(spacer, washer)
spindle hub
spindle shaft woodruff key
Woodruff keys are semi-circular discs used to connect shaft and pulley to rotate together

## Slide 5
Little Bull Loader
https://www.youtube.com/watch?v=FwDi80FUzXU
https://www.littlebuckloader.com
https://www.littlebuckloader.com/shop/p/little-bull-loader-front-end-loader-john-deere
PRICE: $3,300

## Slide 6
Sweeper
Agri-Fab Inc 45-0546 52" Lawn Sweeper, Black
https://www.amazon.com/gp/product/B07KMX858N/
10 Cubic Feet Steel Dump Cart
https://www.amazon.com/dp/B08R95SSTJ
Dump Cart

## Slide 7
Modern JD Loan Tractors
https://www.deere.com/en/mowers/lawn-tractors/
Series S100
42,48,54" wide
$2.4 - $3.6K
Series S200
42,48 wide
$3.3-3.7K
Series X300
42,48" wide
$3.6K - $7.3K
Series X500
48,54" wide
$7.5K - $10K
X700 Signature Series
48,54, 60" wide
gas or diesel
2 or 4-wheel drive
$14K - $17K
Best: X758, $17K
weight 1,032 lbs (470k)