## Slide 1
DIY Rubber Razors, Waterbars: erosion prevention for roads, paths and trails
https://awwatersheds.org/rubber-razors-do-it-yourself-conservation-practices/
https://www.atlasbelt.com/waterbars.php
https://www.atlasbelt.com/conveyor-belt-water-diversions-instructions.php
Water Divert Bar, Rubber Razors
Google for "buy recycled conveyor belt"
https://www.google.com/search?q=buy+recycled+conveyor+belt
https://www.miprcorp.com/conveyor-belts/used-belts/
https://www.repurposedmaterialsinc.com/conveyor-belt/
https://www.repurposedmaterialsinc.com/conveyor-belt/ohio-conveyor-inventory/
Instructions:
https://www.atlasbelt.com/TB_Conveyor_Belt_Diversion.pdf
Recycled conveyor belt (0.5" x ~15" x road width+30%)
2x6" treated lumber.
corrosion resistant bolts, washers, and nuts
12 Bolts 3/8" diam ( 8 short (4"), 4 long (6"))
24 wide washers
12 nuts
You then dig a trench diagonally across the road deep enough to leave approximately 4" of the rubber belt exposed above your gravel road.
Once installed, trucks and other machinery can easily drive over the rubber and will spring back to its original position once they have passed.

## Slide 2
Gravel
https://en.wikipedia.org/wiki/Gravel
Gravel
Crushed Stone
gravel is categorized into :
granular gravel (2–4 mm or 0.079–0.157 in)
pebble gravel (4–64 mm or 0.2–2.5 in)
ISO 14688 grades gravels as
fine - 2–6.3 mm (0.079–0.248 in)
medium - 6.3 – 20mm (0.248 – 0.79 in)
coarse - 20–63 mm (0.79–2.48 in)
One cubic meter of gravel ~ 1,800 kg = 4,000 lb
one cubic yard ~ 1,400 kg = 3,000 lb
For 2 inches depth:
1/4 to 1/2 inch gravel (medium size): 100 square feet per ton
1/2 to 1 inch gravel (more coarse): 90 square feet per ton
1.5-2 inch gravel (coarse): 80 square feet per ton
1/2 inch pebble gravel:
$15-75 per cubic yard
$25-53 per ton
$5-20 per bag
2" Lava Rock (red/brown)
$75-165 per cubic yard
$115-220 per ton
$5-22 per bag
2" River Rock
$45-140 per cubic yard
$60-170 per ton
$5-17 per bag

## Slide 3
How to Drain or Divert Water
Water running down the road makes deep grooves in it.
Water bars and drainage dips every ~10 meters diagonally to divert water to the side. You can use soil+gravel, or a log
https://roadsforwater.org/guideline/water-harvesting-and-drainage-from-unpaved-roads/use-basic-road-surface-drainage/
Drainage Groove Water Drain Ditch
Polymer Concrete Drain
Perforated Drain Pipe
Advance Drainage Systems
drain grate
trench grate
Steel Trench Grating "Sold by the Foot" 1" Thick x 12" Wide https://www.metalsdepot.com/product/3266
Sewer Cover
Rainwater Grate
Trench Cover
Resin Manhole Cover
50cm x 30 cm x 2 cm
$44 at Walmart & Amazon