## Slide 1
Oil - 550 Gallon Tank
Delaware Valley Oil
http://dvoil.com
Phone (845)-887-6090
Office: M-F 8am-4pm
3 Bridge Street, Callicoon, NY 12723
P.O. Box 838 Callicoon NY 12723
Email delawarevalleyoilllc@yahoo.com
Email: LeanaStanton@aol.com
Owner wife: Casey Milk
Truck driver: Larry, Kevin
Service?
Cleaning?
Brian
845-645-9403 cell
Plumber
(Boiler/Filter mainenance)
2022-07-06: ordered 150 gal ($5.79/gal) = $868.50
2022-11-22: ordered 150 gal ($5.59/gal) = $838.50
2023-01-07: gauge reading: 1/4 = 108 Gal
2023-01-07: ordered 150 gal ($4.29/gal) = $643.50
2023-01-14: gauge reading: 1/2 = 275 Gal
2023-02-05: gauge reading: 3/8- = 175 Gal
2023-02-10: ordered 250 gal ($4.19/gal) = $1,047.50
2023-02-11: gauge reading: 3/4+ = 455 Gal
2023-05-30: ordered 200 gal ($3.52/gal) = 465 gal
2024-01-07:gauge reading:1/4+(120 gal)
2024-01-11: ordered 331.6 gal @ $3.86/gal – full
2024-07-16: ordered 300 gal @ $3.76
DJS Plumbing and Heating
Doug Santoro
(845) 887-6309 office
(845) ... mobile
email: djsph@hvc.rr.com
.. https://www.djsph.com
.. https://www.facebook.com/DJSPlumbingHeating/
.. 9 Del Vue Rd, Callicoon, NY 12723
.. 4-6 weeks waiting for scheduled service
Hook Well Drilling. 570-224-....
Head Electric Plumbing & Heating, Inc
(845) 807-7676
4499 St Rt 17B, Callicoon, NY 12723
pat costello plumbing PA. 570-224-....

## Slide 2
Calculator:
https://www.mathsisfun.com/geometry/cylinder-horizontal-volume.html
Oil Tank 48" diameter, 550 gal
inch | part | part | gals | inch | part | part | gals
1 | 0.02 |  | 3 | 25 | 0.52 |  | 290
2 | 0.04 |  | 8 | 26 | 0.54 |  | 304
3 | 0.06 |  | 14 | 27 | 0.56 |  | 319
4 | 0.08 |  | 22 | 28 | 0.58 |  | 333
5 | 0.10 |  | 30 | 29 | 0.60 |  | 347
6 | 0.13 | 1/8 | 40 | 30 | 0.63 | 5/8 | 362
7 | 0.15 |  | 50 | 31 | 0.65 |  | 376
8 | 0.17 |  | 60 | 32 | 0.67 |  | 390
9 | 0.19 |  | 71 | 33 | 0.69 |  | 403
10 | 0.21 |  | 83 | 34 | 0.71 |  | 417
11 | 0.23 |  | 95 | 35 | 0.73 |  | 430
12 | 0.25 | 1/4 | 108 | 36 | 0.75 | 3/4 | 442
13 | 0.27 |  | 120 | 37 | 0.77 |  | 455
14 | 0.29 |  | 133 | 38 | 0.79 |  | 467
15 | 0.31 |  | 147 | 39 | 0.81 |  | 479
16 | 0.33 |  | 160 | 40 | 0.83 |  | 490
17 | 0.35 |  | 174 | 41 | 0.85 |  | 500
18 | 0.38 | 3/8 | 188 | 42 | 0.88 | 7/8 | 510
19 | 0.40 |  | 203 | 43 | 0.90 |  | 520
20 | 0.42 |  | 217 | 44 | 0.92 |  | 528
21 | 0.44 |  | 231 | 45 | 0.94 |  | 536
22 | 0.46 |  | 246 | 46 | 0.96 |  | 542
23 | 0.48 |  | 260 | 47 | 0.98 |  | 547
24 | 0.50 | 1/2 | 275 | 48 | 1.00 | "1" | 550
Krueger Sentry Therma Tank Gauge
https://www.jmesales.com/krueger-sentry-type-h-2-in-galvanized-therma-tank-gauge/

## Slide 3
Peerless Boiler WB-3 Series (WBV-110-WPD ?)
residential, oil-fired boilers
https://www.peerlessboilers.com
https://www.peerlessboilers.com/products/series-wbv/
https://www.youtube.com/watch?v=5GbXgEYw5TE
12-18 Gal of water
Honeywell boiler aquastat (thermostat)
sends "more heat" signal
to 7505 burner control unit
Beckett GeniSys™ 7505 oil burner control https://www.beckettcorp.com/product/genisys-7505-oil-burner-control/
used with a suitable cad cell flame sensor to control the oil burner motor, igniter, and optional solenoid valve
has 24 VAC thermostat terminals
can provide interrupted or intermittent duty ignition, and it has a 15 second lockout time
Specific model 7505A

## Slide 4
Boiler
https://www.peerlessboilers.com
https://www.peerlessboilers.com/products/series-wbv/
Water Pressure in kitchen sink – 40-60 PSI
Water Pressure in house heating should be low (15 psi ?)
Test – time to fill a 5 Gal bucket
(20 sec – excellent, 60 sec – fine)

## Slide 5
(Re) Starting Boiler
How to Replace An Oil Filter For Your Oil Fired Boiler Or Furnace
https://www.youtube.com/watch?v=yx9g9P_z5So
How To Restart An Oil Furnace | Hard Lockout and Bleeding Fuel Lines
https://www.youtube.com/watch?v=TUKQ02AVtz0
Oil Heat Boilers - How it works - the Basics
https://www.youtube.com/watch?v=5GbXgEYw5TE
Oil Heat Boilers - How it works - Understand the Basics
https://www.youtube.com/watch?v=5GbXgEYw5TE
How To Prime and Restart an Oil Heater After Oil Is Empty
https://www.youtube.com/watch?v=YMvrSXqZdiQ
How to bleed oil burner, restart, re-light the furnace
https://www.youtube.com/watch?v=gZcPUH83S10
Plugged Oil Line to Boiler Furnace and Filter Change DIY
https://www.youtube.com/watch?v=tj_3pXc2rZM
How to bleed the oil furnace
https://www.youtube.com/watch?v=DFY10lAQM28
Oil furnace troubleshoot part 4 no oil to burner
https://www.youtube.com/watch?v=NT6mMApZES0
Setting electrodes and replacing nozzle
https://www.youtube.com/watch?v=N6i2x08oI4o
Common Burner Issues and How to Fix Them
https://www.youtube.com/watch?v=svP6khjS1xQ
1A-25A filter housing – older model (that we have).
1A-25B – newer model, has epoxy coating on the inside of the housing to prevent corrosion caused by contaminants in the oil.
S264 – yet another compatible cartridge
All above housings use the same filters/cartridges.
General 1A-30. Search for "Replacement for 1a-30 Fuel Oil Heat Filters Cartridge" on amazon, etc.
Typically 10-micron Wool Felt Filters

## Slide 6
Replacing Nozzle
https://www.youtube.com/watch?v=dCtwGjH8gcw
shut-off electrical switch for the boiler
shut the oil line off
unscrew 2 screws and pivot black transformer box
disconnect oil metal tube
take out electrodes' assembly (careful not to spill oil)
degrease everything
unscrew – and change the nozzle
position tips of electrodes properly
assemble back
Nozzle: "00085-80B1" or .85-80B
0.85 - flow rate (in gal/hr at 100PSI)
80 - spray angle of the nozzle (degrees)
B - spray pattern (solid cone)
https://www.amazon.com/gp/product/B000VB6C5K/
Honeywell 120320 Cad Cell
https://www.amazon.com/gp/product/B004P646DC/
Allanson Oil Burner Ignition Transformer 2721-628g
https://www.amazon.com/dp/B082J42D88/
Beckett 51771u
PowerLight Igniter
(modern drop-in replacement for an ignition Transformer)

## Slide 7
Google for:
Genisys 7505 won't start after power outage
Video troubleshooting the 7505
.. https://www.youtube.com/watch?v=Wd7vrkUDaz4
Troubleshooting Beckett Genisys 7505
Checks for flame presence
Ignites – and checks that it is ignited
reacts to signal "more heat" to start/stop blower (and shut off the valve)

## Slide 8
Honeywell Aquastat
Honeywell Boiler Aquastat
Model L8124C1102
The aquastat has a temperature-sensing element.
It has a 120V/24V AC transformer
It has electronic relays for burner and "circulator pump" circuits:
.. Activate the burner to heat the water if T is too low
.. Shut off the boiler at high water temp.
.. Turn on the circulator pump when T is high enough

## Slide 9
Taco SR503-EXP Switching Relay
Taco SR503-EXP - 3 zone expandable switching relay (bought Sept 2021)
The Taco SR503-EXP is a switching relay used in hydronic heating systems. Here's a breakdown of its key functions:
Zone Control:
  It manages and controls multiple heating zones within a building. In the case of the SR503-EXP, it handles 3 zones, and is expandable to handle up to 20.
Relay Switching:
  It uses relays to switch on and off the circulator pumps that distribute hot water to different heating zones. This is in response to signals from thermostats.
System Customization:
  It allows for system customization through features like switchable priority, which allows a designated zone to receive heating priority over others.
Diagnostic Feedback:
  External indicator lights provide visual feedback for diagnostics, making installation and troubleshooting easier.
Expandability:
  The "-EXP" designation indicates that it's expandable, meaning it can be connected with other Taco switching relays to control a larger number of heating zones.
Compatibility:
  It's designed to be compatible with conventional and programmable thermostats.
PowerPort Capability:
  It has PowerPort slots that allow for the addition of PowerPort cards, which add enhanced functions to the system.
In essence, the Taco SR503-EXP is a control center that coordinates the operation of a zoned hydronic heating system, providing flexibility and control over how heat is distributed throughout a building.

## Slide 10
Google Nest Thermostat:
.. https://store.google.com/us/product/nest_thermostat
Nest Wifi requires a Nest Wifi router (or Google WiFi)
Latest - Nest Wifi Pro router ($200)
The devices are controlled using Google Home App
Google Nest Thermostat - 1
https://www.cnet.com/home/internet/nest-wifi-vs-nest-wifi-pro-wi-fi-6e-mesh-routers/
https://www.doityourself.com/forum/thermostatic-controls/602985-connecting-nest-thermostat-genisys-7505-oil-burner.html
https://www.youtube.com/watch?v=WFDPWIKKBHY
.. https://store.google.com/us/widget/compatibility/thermostat
Google Nest thermostats are designed to work with most 24 V systems, even older systems
Online Compatibility Checker: .. https://support.google.com/googlenest/answer/9246656
Nest Learning Thermostat is more compatible
Older Regular Nest Thermostat may need C wire or Nest Power Connector
Note about Nest Learning Thermostat.
It has many settings to automatically adjust temperature based on history, etc.
I turned them all off because it was overriding my wishes. For example, we had two bedrooms with thermostats. Last several weeks we had visitors and were using both bedrooms. This week we using only one, so I decreased the thermostat setting to 56F. But it by itself warmed up to 68F.
We have the latest Nest Learning Thermostat (3rd generation) I was following youtube videos and online guides, for example:
.. https://support.google.com/googlenest/answer/9248184 - docs .. https://support.google.com/googlenest/answer/9373007?hl=en – PDFs
.. https://www.youtube.com/watch?v=rdfUbAZi7k0 – missing manual .. https://www.youtube.com/watch?v=7SzjOU30AYg - How to Use ... .. https://www.youtube.com/watch?v=iXi8asdsXTM – How to Use ... for beginners .. https://www.youtube.com/watch?v=AdGDXpb4VzE - How to Use and Program ... .. https://www.youtube.com/watch?v=iKcSKpR9KAM - How to Make Nest Thermostat Manual
(remove learning automation parts)

## Slide 11
.. https://www.youtube.com/watch?v=iKcSKpR9KAM
How to Make Nest Thermostat Manual
Go to Settings
Nest Sense
Auto Schedule
No (to learning)
DONE
ECO
off both
Home Away Assist
STOP Using ECO
RESET
Schedule
Reset
Turn right to reset
Google Nest Thermostat - 2

## Slide 12
https://www.youtube.com/watch?v=eM_2CXz45RE
Nest Thermostat Loses WiFi Randomly
Check WiFi stability and speed
Turn router off for 30 sec – and then turn on again
Check that battery level > 3.6V
Reset-Restart the Thermostat
After restarting check Network settings in the Thermostat
ping speed should be < 1500 ms
ping speed == 0 – no communication with server
signal strength should be > 50
Reset Network Settings
Install updates on your Thermostat
Install updates on phone app
Use the interactive Guide: https://widgets.nest.com/nest-thermostat-troubleshooter/
Contact Google Nest Help: Twitter @GoogleNestHelp
Google Nest Thermostat - 3

## Slide 13
Water Heaters:
Heating the house (~15 psi) – Oil Boiler
small (12-18 Gal) water camera
low water pressure (below 15-30 psi)
Heating water in sinks and showers (40-60 psi)
Tankless - water passes through coil which is heated by the natural gas furnace
Storage water heater – has 50-80 gal tank heated by natural gas, electric, hybrid (electric direct + compressor), or indirect (heated by hot water from boiler). Usually has a thermal insulation and a thermostat
Storage water heater:
Tankless water heater:
Tankless water heater
is better than storage tank:
never run out of hot water
efficient and economical
maintenance once per year
can last 20+ years
Selecting a New Water Heater
https://www.energy.gov/energysaver/selecting-new-water-heater

## Slide 14
Water Heaters - Tankless
Tankless water heaters:
https://www.youtube.com/watch?v=_RZ3IVK2p5Q -
https://www.youtube.com/watch?v=vRUgFmBaSCM -
https://www.youtube.com/watch?v=8RFuFBI3r2c –
https://www.youtube.com/watch?v=Ax5yrRgtKMs – tank vs tankless
https://www.homedepot.com/p/325308951 – Rheem
https://www.youtube.com/watch?v=T4FaqGod3VU – DeScaling
https://www.amazon.com/dp/B0084CPDFS - Rheem RTGH-95DVLN 9.5 GPM Indoor Direct Vent Tankless Natural Gas Water Heater
https://www.amazon.com/dp/B07CW426QZ - Rinnai RU199iN Condensing Tankless Hot Water Heater, 11 GPM, Natural Gas, Indoor Installation, small, Japan, reliable, 90 years, 50% of market - https://www.youtube.com/watch?v=F-AfoaaV1UM -
Tankless water heater is better than storage tank:
It only works when you using it
Never run out of hot water
Efficient and economical
Maintenance once per year (flush/descale)
Can last 20+ years
Condensing Tankless Water Heaters – capture heat from the exhaust gases through a secondary heat exchanger – and use it to pre-heat the incoming cold water.
This significantly reduces the gas bills.
Also the temperature of the output exhaust is low, so you can use cheap easy to install PVC or CPVC pipes instead of stainless steel.
But the extracted heat creates condensate, which need to be disposed of, typically to a floor drain or sewer system.
Burning Natural Gas models vs Electric:
Burning natural gas delivers higher flow rates, providing hot water faster and in larger quantities
It is also more cost-effective to operate in the long run
Requires a vent for exhaust (any maybe floor drain for condensate)
Service Valves (red and blue) for hot and cold water – allow to flush/de-scale the heater once a year (with vinegar or special solution)
an expansion tank is generally not required for a standard tankless water
tank
tankless
Installing
Condensate
Neutralizer
https://www.youtube.com/watch?v=RfjnOPrvGwA
Average shower flow is 1.5 gal/min flow
(rated at 2.5 gal/min at 80 psi,
but average water pressure is 60 psi)

## Slide 15
Hybrid systems:
.. https://www.youtube.com/watch?v=wt95SE2ogNI – buying guide, 2022
.. https://www.youtube.com/watch?v=q3Rovg4cyyY - top 5, 2020
Rheem - ProTerra Electric Hybrid (Gen 4) (HomeDepot) .. https://www.rheem.com/innovations/innovation_residential/hybridsavings/ -
A.O. Smith - Signature Series ( buy at Lowes) .. https://www.aosmithatlowes.com/products/water-heaters/electric-water-heaters/hp10-80h45dv/ - .. https://www.youtube.com/watch?v=6D7KOGIsoCs – installation
Bradford White – AeroTherm .. https://www.bradfordwhite.com/aerotherm/
Sanden - SanCO2 .. https://www.smallplanetsupply.com/sanc02
Stiebel Eltron – Accelera (German, expensive) .. https://www.stiebel-eltron-usa.com/products/accelera-heat-pump-water-heaters -
Water Heaters with Storage Tank
Indirect water heaters (like SuperStor ULTRA 316 Liters) use hot water from boiler going through the coil to heat the tank.
https://www.htproducts.com/superstor-ultra-waterheater.html
Maintenance tricks:
Clean air filter every month, add additional pre-filter on the top
https://www.youtube.com/watch?v=21AuJYRhk5o
https://www.youtube.com/watch?v=mwrwJoS-7K8
https://www.youtube.com/watch?v=v_Wqig8WjVA
Use Corro-Protec™ Powered Anode Rod
Heat Pump Water Heaters – work as reverse refrigerator, use electricity to move heat from outside to the tank. They don't generate heat directly. They can be 2-3 times more energy effective.
.. https://www.energy.gov/energysaver/heat-pump-water-heaters –
Hybrid systems – use Direct Heater and a Heat Pump.
The heat pump can be added to an existing system where the direct heater may be electric, natural gas, indirect from boiler.
If buying new system – purely electric is probably better.

## Slide 16
Electric Space Heaters
Best Space Heater? Safest and Deadliest?
https://www.youtube.com/watch?v=hynRbnQ2hIE
Dreo Space Heater
$38
Dr. Heater
$100