## Slide 1
Estimated Water Usage
50-100 gallons per person per day (up to 3,000 per month)
washing machine: 30 gallons per load
kitchen sink: 3 gallons per minute
Bathroom Sink: 2 gallons per minute
Shower: 5 gallons per minute
Estimating water usage – 400 gallons per day we are in the house.
Per year we spend 114 days: (50 weeks * 2 days) + (2 weeks * 7 days)
Per year: 114 days * 100 gallons * 4 people = 40,000 gallons/year
sediment filter lasts 10K gallons – change every 3 months

## Slide 2
Water Cleaning System
Fritz Bros., Inc.
Well drilling, plumbing,
water-softening
Address: 100 Cliff St,
Honesdale, PA 18431
Phone: (570) 253-2660
Hours: Mon-Sat 7am-4pm
Step2
Mark 10
Bonded Glass-Lined Standard Tank
Step1
Flex Lite Tank
(35 galons, 2018)- store/ deliver water under pressure between pumps
https://flexconind.com/product/flex-lite-series/
max working pressure 125 PSI (pexB tubes – 160 PSI)
Step0
goulds pumps bruiser submersible pump
Model 7SB05422C
with 230V motor (1/2 horse power)
4" Submersive Pump from ITT Gould Pumps
7 gallons per minute
.. https://goulds.com
.. https://www.gouldspumps.com
Max pressure: 125 PSI
Typical operating pressure: up to 60 PSI
Also Deep Well
Merrill AE-10 Air Ejector Control
Step3
Aqua-Pure Iron and Manganese Reduction System Model APIF100DM
SN 613114A519
Installed 2014
Serviced 10/2018, 8/2020
W M Fulton & Son Well Drilling
Eugene & Karen Fulton
456 Old Taylor Rd, Jeffersonville, NY 12748
845-482-3335 Patty mother
845-791-0516 Eugene mobile
May 2025 – inspected,
added chlorine tablets,
estimated depth as 150 ft
can see water at 40 ft down

## Slide 3
Water flow measuring and shut-off
thinking about buying the FLO by Moen:
Moen 900-001 Flo Smart Water Monitor and Automatic Shutoff Sensor, Wi-Fi Water Leak Detector for 3/4-Inch Diameter Pipe - $350
https://www.amazon.com/dp/B00C03D01Q It can monitor water usage, alert and automatically shut-off in case of leaks

## Slide 4
Why the water is blue blue after Aqua-Pure APIF100DM ?
If the water appears blue after passing through the Aqua-Pure APIF100DM system, it could indicate one of the following issues:
Copper Corrosion: Blue or greenish water is often caused by copper leaching from plumbing pipes or fixtures. This can happen if the water is too acidic (low pH) or if the system is not properly neutralizing the water.
Oxidation Reactions: The system may be oxidizing certain metals or minerals in your water supply, which could give the water a bluish tint. This could occur if there are trace amounts of copper, manganese, or other metals in the water.
Contamination or Residue in the System: If the system has not been flushed properly after installation, maintenance, or regeneration, residual chemicals or media fines (e.g., manganese dioxide) might discolor the water.
Steps to Address the Issue:
Test Water pH: Check if the water pH is within the recommended range (6.5–8.5). If it is too acidic, consider installing a pH neutralizer.
Inspect Plumbing: Look for signs of copper corrosion in your pipes and address any issues with a plumber.
Flush the System: Perform a thorough flush of your system to remove any trapped air, fines, or residue from the filter media.
Check for Maintenance Needs: Ensure that all components of your system are functioning properly and that regeneration cycles are being conducted as recommended.
Consult a Professional: If the issue persists, contact a water treatment specialist to inspect your system and analyze your water for potential contaminants like copper or other metals.
products of copper oxidation :
- Malachite (dark green to blue)
- Azurite (blue to purple)
Copper oxide or carbonate, formed through prolonged exposure to moisture and air.
pH measurement:
https://www.amazon.com/dp/B077Z6LF91
APERA INSTRUMENTS AI209-T Value Series PH20 pH Tester Combo Kit

## Slide 5
Whole House Water Filter
The WH-HD200-C housing 1 inch outlets (with bracket)
https://www.amazon.com/dp/B01JIRLRXY - housing
Filter for it:
Culligan RFC-BBSA 25 Micron Whole House Water Filter for Sediment, 10" x 4.5"
https://www.amazon.com/dp/B000BQN6MM – filter
Whole House Water Sediment Filter (25 micron)
Reduces sediment, dirt, sand, silt, and rust particles down to 25 microns.
Typically made of polypropylene or similar materials.
Often used as a first stage in whole house filtration systems.
Filter life: Usually 3-6 months or 20,000-60,000 gallons, depending on water quality.
Does not address chemical contaminants or dissolved minerals.
Aqua-Pure Iron and Manganese Reduction System (APIF100DM)
Reduces iron, manganese, and adjusts pH.
Uses a chemical-free process to reduce ferrous (dissolved) and bacterial iron.
Incorporates air induction for iron oxidation.
Includes a bypass valve with multiple positions, including a diagnostic mode.
Designed for high iron content in water and hydrogen sulfide gas reduction.
More complex system compared to simple sediment filters.
Addresses specific water quality issues beyond just particulate matter.

## Slide 6
Iron & Manganese Removal
Our house uses 40,000 gallons of water per year. We currently have old Aqua-Pure APIF series residential iron and manganese reduction system Model APIF100DM. It was installed in 2014. The model was discontinued in 2016. It is a big tank filled with media that can last for 2-3 years before service appointments.
We can substitute it with a smaller wall-mounted system that uses replaceable cartridges. This change would offer several advantages: Space-saving, Easy DIY maintenance, cost effective (overall).
Example: multi-stage filtration system like the iSpring WGB32BM
- https://www.amazon.com/dp/B01FI3BLYM - $426
- https://www.youtube.com/watch?v=MSv1jDHGU_c – video description
- https://www.youtube.com/watch?v=svoIxJYPTXo - recent description (does not remove arsenic)
- https://www.amazon.com/dp/B0776ZLQ1V - replacement filters ($106)
- It has 3 stages of filtration, including specialized iron and manganese removal stage 1st stage is a 5 micron sediment filter, 2nd stage – carbon filter, 3rd stage – specialized filter (Fe, Mg)
- Can handle up to 100,000 gallons before replacement
- Is wall-mounted and easy to install
- supports water flow up to 15 gallons per minute
| Feature | Aqua-Pure APIF100DM[1][3] | iSpring WGB32BM[4][6] |
|------------------------|------------------------------------------|----------------------------------------|
| Iron Reduction | Handles high iron concentrations | Reduces from 3.0 ppm → 0.01 ppm |
| Manganese Reduction | Effective for manganese removal | Reduces from 1.0 ppm → 0.01 ppm |
| Process | Air-induced oxidation with MC-10MP media | Catalytic filtration (FM25B cartridge) |
| Max Contaminant Levels | Not explicitly stated | Iron ≤3 ppm, Manganese ≤1 ppm |
| pH Adjustment | Built-in capability | Requires pre-adjusted pH water |
| Flow Capacity | 6 GPM | 15 GPM |
| Maintenance | every 2-3 years | every 6-12 months |
| Installation | Large floor-standing tank | Compact wall-mounted system |
| Ph level | adjusts automatically | |
| High Contaminant Levels| may be better ? | |
Note:
Manganese (Mn): Atomic # 25, transition metal
Magnesium (Mg): Atomic # 12, alkaline earth metal
Iron (Fe): Atomic # 26

## Slide 7
Water Testing April 2025
ND = Not Detected
D = Detected above reporting limit
Metal | Result | Limit | Standard | Units | Safe Level (EPA/NY) | ppm | Too High? | Comments | in | out
Aluminum | 120 | 2 | 40 | µg/L | <50-200 µg/L (SMCL) | 0.12 | Borderline | Slightly above the NY standard (40 µg/L), but below EPA’s SMCL (Secondary Maximum Contaminant Level) of 50-200 µg/L. Not a primary health risk, but may cause taste/color issues. |  | 
Iron | 0.61 | 1 | 0.10 | mg/L | <0.3 mg/L (SMCL) | 0.61 | Yes | Above EPA’s SMCL for iron (0.3 mg/L). Not a health risk, but can cause staining and taste issues. | 1.2 | 0.55
Arsenic | 1.9 | 1 | 1.4 | µg/L | <10 µg/L (MCL) | 0.002 | No | Well below EPA’s MCL (10 µg/L). Safe. |  | 
Cadmium | ND | 1 | 0.50 | µg/L | <5 µg/L (MCL) | 0 | No | Not detected. Safe. |  | 
Cobalt | ND | 1 | 1.0 | µg/L | No EPA standard | 0 | No | Not detected. No standard. |  | 
Copper | 170 | 1 | 35 | µg/L | <1,300 µg/L (AL) | 0.17 | No | Well below EPA’s action level (1,300 µg/L). Safe. |  | 
Lead | 7.77 | 1 | 1.00 | µg/L | <15 µg/L (AL) | 0.008 | Yes | Above NY standard (1.00 µg/L) and EPA’s goal (0 µg/L). EPA’s action level is 15 µg/L, but any lead is a concern, especially for children. Should be as low as possible, ideally below 1 µg/L. | 11.4 | <1
Manganese | 530 | 10 | 50 | µg/L | <300 µg/L (SMCL) | 0.53 | Yes | Above EPA’s SMCL (300 µg/L) and NY standard (50 µg/L). Can cause taste, color, and potential health effects at high levels. Should be below 50 µg/L for NY, and below 300 µg/L for EPA. | 545 | 660
Molybdenum | ND | 1 | 1.0 | µg/L | No EPA standard | 0 | No | Not detected. No standard. |  | 
Nickel | 1.6 | 1 | 0.50 | µg/L | <100 µg/L (Health) | 0.002 | No | Well below health advisory. Safe. |  | 
Tin | 1.3 | 1 | 1.0 | µg/L | No EPA standard | 0.001 | No | Slightly above reporting limit, but no standard. |  | 
Uranium | ND | 1 | 1.0 | µg/L | <30 µg/L (MCL) | 0 | No | Not detected. Safe. |  | 
Zinc | 73 | 1 | 20 | µg/L | <5,000 µg/L (SMCL) | 0.07 | No | Well below EPA’s SMCL (5,000 µg/L). Safe. |  | 
Note:
Manganese (Mn): Atomic # 25, transition metal
Magnesium (Mg): Atomic # 12, alkaline earth metal
Iron (Fe): Atomic # 26
1 ppm = 1 mg solute / 1 kg solution = 1 mg/L

## Slide 8
Installing on the wall
Hardboard Pegboard (kit) from Lowe's
Wall Control Pegboard Kit
Plywood attached to vertical metal studs

## Slide 9
Iron & Manganese whole-house Removal
Moen 900-001 Flo Monitor/Shutoff - https://www.amazon.com/dp/B00C03D01Q
iSpring WSP50ARB - 50 micron, Auto Flushing Module - https://www.amazon.com/dp/B07XLP2T2Y
Rusco 2" 100 Mesh Spin Down Sediment https://www.amazon.com/dp/B005FYN8GE
iSpring WGB32BM 3-stage filtration - https://www.amazon.com/dp/B01FI3BLYM
iSpring WGB12B 1-stage post-filter - https://www.amazon.com/dp/B0785FZYM3 (or 2nd 3-stage filter)
iSpring WCFM400K Iron and Manganese Water Filtration with regeneration https://www.amazon.com/dp/B09L9HBWRX
sed25, sed5, carbon
Fe/Mg, Fe/Mg, carbon
Flo Monitor/Shutoff
Auto-Flushing Sediment Filter
or
Rusco Spin Down Filter 2- inch
Aqua-Pure Fe/Mg
Reduction System
Model APIF100DM
or
iSpring WCFM400K Whole House Central Iron and Manganese Water Filter Filtration System
https://www.amazon.com/dp/B09L9HBWRX

## Slide 10
3' x 7'
Wall Mount
Carbon, Sed5, sed25
Carbon, Led, Fe/Mn
Flo Monitor / Shutoff
The iSpring WGB32BM 3-stage
whole house filtration system
horizontal: 24.5 inches
height: 28.0 inches
depth: 8.0 inches
need extra space for connections
The iSpring WGB32BM 3-stage
System 2: (output)
Stage 1: FM25B Iron/Manganese removal (50K gal)
Stage 2: FM25B Iron/Manganese removal (50K gal)
Stage 3: FCTO25B CTO Carbon – (100K gal) – final stage
System 1 (input)
Stage 1: FP25B Sediment Filter 5 microns (100K gal)
Stage 2: FG25B-KS GAC+KDF Filter (150K gal)
Reduces chlorine, hydrogen sulfide, ...
Stage 3: FC25B-PB Lead-Reducing Filter (100K gal)
As our usage is less than 40K gal/year, we can change Iron/Manganese filters once per year, and other filters once per two years)
iSpring WSP50ARJ-BP Spin-Down Sediment prefilter with Bypass, Flushable & Reusable

## Slide 11
Unscrew filter
How to unscrew stuck filter
https://www.youtube.com/watch?v=BcTaSyBiD78
https://www.youtube.com/watch?v=MUtF_lXAExM
plastic wrench (comes with filter)
two plastic wrenches
bigger metal wrench (check size: https://www.amazon.com/dp/B00IOUEFL8
use tube on handle for more leverage
lisle+strap+wrench - https://www.amazon.com/dp/B007QVB71C (or flat strap and two spaners)
use silicone grease - https://www.amazon.com/dp/B0081JE0OO

## Slide 12
Reverse Osmosis (RO) filtration systems are widely used in homes for drinking/cooking water
Pros of RO:
High Contaminant Removal (99%) including heavy metals (lead, arsenic), nitrates, bacteria, viruses, and PFAS. They filter particles as small as 0.0001 microns, providing extremely pure water.
Improved Taste, convenience, cost-effective over time
Cons of RO:
Loss of Minerals (Ca, Magnesium,...)
wastes anywhere from 0.2 to 5 liters per 1 liter of purified water
Filters need replacement every 6-12 months
Pressure drop ?
RO – Reverse Osmosis Systems
https://www.youtube.com/watch?v=vN2R2pi7eYc
prefiltration
post-filtration (carbon0
re-mineralization cartridge
enough capacity for flow
enough capacity for duration
booster pump to keep high pressure
efficiency
maintenance – parts cost
filters should be standard size – allowing to use cheap 3rd party filters
is it upgradable?
use a system with a tank, stay away from tankless systems
freshwatersystems.com
Best 3 whole-house RO systems:
https://www.youtube.com/watch?v=9zzfOtBVcjA
US Water Systems Defender Whole House Reverse Osmosis System
https://www.youtube.com/watch?v=9zzfOtBVcjA - $10,000
Crystal Quest Whole House Reverse Osmosis System - $2,500
https://crystalquest.com/products/whole-house-reverse-osmosis-system
iSpring RCB3P Reverse Osmosis RO Water Filtration System, 300 GPD, Tankless, $550 - https://www.youtube.com/watch?v=YfRQmJdun54
https://www.amazon.com/dp/B007K1FDJA
Tankless Reverse Osmosis Systems:
.. take less space, continuous on-demand water supply, reduced water waste, water is fresh, advanced features like integrated TDS meters, LED indicators, filter status indicators
.. but ... require constant electricity to operate (no tank), may need additional pump, TDS Creep (dirty water in first few seconds before pressures is built). TDS = Total Dissolved Solids

## Slide 13
Good overview of how well and tanks work together: .. https://www.youtube.com/watch?v=X4TZoFIsE2w
Check valve (passes water only in one direction)
"Tank-T" or "Well-T" or "Well Manifold" The gauge shows pressure as it goes up/down Pressure switch turns pump on/off Safety switch (safety valve) to release pressure above ... (75 psi ?)
Tank-T assembly with pressure gauge and pressure regulator
https://www.amazon.com/Harvard-Boshart-installation-Pressure-pressure/dp/B078WCYK88
$115

## Slide 14
Tank-T Pressure Adjustment
Video showing how to regulate the pressure:
https://www.youtube.com/watch?v=1VNSv7xVzzU
Turn #1 3.5 full turns clock-wise
to increase pressure by 10 PSI

## Slide 15
Why WellXTrol is the BEST Water Well Pressure Tank.
(150 PSI)
.. https://www.youtube.com/watch?v=MmHRJSzZltI
How WellXTroll tanks are made
.. https://www.youtube.com/watch?v=IhBifh7nCtg
Shop Amtrol Well-X-Trol tanks ($700-$1,000):
.. https://www.rcworst.com/Amtrol/Well-X-Trol-c225.html
The recommended pressure is 40-60 psi.
If tank and pressure switch are in the basement,
and the water sink is upstairs 5 meters up,
we will lose 5 m * 1.421 psi = 7.1 psi
Pressure decrease due to elevation:
0.433 psi per foot of elevation
1.421 psi per meter of elevation
So, we need at least 50 psi downstairs
to ensure at least 40 psi upstairs.
Standard garden hose in the US has a female connector designed to screw onto the male 3 / 4 inch spigot (tap) with NHT (National Hose Thread).

## Slide 16
Problem: opening water in the bathtub results in a weak water stream in the sink
Possible reason: water pressure or the plumbing system design (narrow and bent tubes).
Water Pressure: should be around 40-60 psi (pounds per square inch).
You can measure the water pressure using a pressure gauge attached to a spigot outside the house.
Solutions:
- Changing pipes (larger is better)
- Installing a Water Pressure Booster System can help.
- Bigger Water Tank might help if water supply is running low quickly
- Checking for Leaks or Blockages that could reduce the pressure.
Pressure Gauge 100 Psi
3/4" Female connector
Camco Water Bandit
Flexible Silicone-Polymer Sleeve & ABS Male Water Hose Connection

## Slide 17
Aqua-Pure
Iron and Manganese Reduction System
Model APIF100DM
SN 613114A519
Serviced 10/2018, 8/2020
Looks like it needs "regeneration"
(press buttons as instructed for few seconds)

## Slide 18
HARVARD
The American Granby Company, Liverpool, NY
7652 Morgan Rd, Liverpool, NY 13090
https://www.americangranby.com/
MARK 10
Bonded Glass-Lined Standard tank
Glass-Lined
Dual Cathodic Protection
Hydro-Pneumatic Pump Tank
The big blue tank in the middle
Previous owners used it many years ago to clorinate the water. Then they stopped doing this.
But didn't remove the tank.

## Slide 19
Types of Tubing
Material | Nominal Size | Outer Diameter (OD) | Inner Diameter (ID) | Notes
Copper (Type L) | 1/2" | 0.625 (5/8") | 0.545 | Type L is common for residential water. OD follows CTS.
Copper (Type L) | 3/4" | 0.875 (7/8") | 0.785 | Type L is common for residential water. OD follows CTS.
Galvanized Steel (Sch 40) | 1/2" | 0.84 | 0.622 | Assumed Schedule 40. Historically used, less common now. OD is larger.
Galvanized Steel (Sch 40) | 3/4" | 1.05 | 0.824 | Assumed Schedule 40. Historically used, less common now. OD is larger.
PEX (SDR9) | 1/2" | 0.625 (5/8") | ~0.485 | OD follows CTS. SDR9 is common. ID is notably smaller than 1/2" copper.
PEX (SDR9) | 3/4" | 0.875 (7/8") | ~0.681 | OD follows CTS. SDR9 is common. ID is notably smaller than 3/4" copper.
- copper used for tubes
- brass used for fittings (stronger than copper)
- cast iron – for drainage
- galvanized pipes – in old buildings
- stainless steel – the best, but more expensive
- PVC – non-potable water, drainage, electrical conduits
- PEX – potable water, heating systems, ...

## Slide 20
Copper tubing nominal size is internal size:
1 / 2 inch internal = 5 / 8 external
3 / 4 inch internal = 7 / 8 external
===================
torch for soldering using MAPP gas (MAP-Pro) (propane is not hot enough)
- Bernzomatic Trigger Start Torch ( TS8000 ),
- Rothenberger 35645M Quick fire torch ===================
clean outside - mesh sand cloth - https://www.amazon.com/dp/B081BMNG6B clean inside ("fitting" brush) - https://www.amazon.com/dp/B08YS56F4Z/
plumbing flux + brush + solder - https://www.amazon.com/dp/B0BSYD1J7J/
tube cutter - https://www.amazon.com/dp/B001P307PO
copper pipe electric grinder cutter - ...
do not try to re-solder the bad connection – cut it off
buy set of copper tubes and couplings 1/2 and 3/4 inch (straight, angled, converters)
cut tube with special cutter or electric grinder, clean with a file, then with mesh/brush, cover with flux, and immediately do the soldering. Overlap approx one diameter. Heat from outside
Work in thick gloves (to remove extra solder)
Stores:
PlumbersStock
PipingNow
SupplyHouse
Home Depot
Lowe's
Plumbing

## Slide 21
#1 PEX Plumbing Mistake You Don't Want to Make (A vs B)
https://www.youtube.com/watch?v=CWgaP90CGmo
https://www.youtube.com/watch?v=DyVRnk0LJzc – best Expansion tools
Pex Plumbing
PEX plumbing systems are widely used due to their durability, cost-effectiveness, and ease of installation. There are two types: PEX-A and PEX-B
PEX-A – made using the Engel (peroxide) method, which results in the highest flexibility and elasticity. Allows tight bend radii without additional fittings. It also has "thermal memory," enabling kink repairs with heat
PEX-B - Formed using the silane (moisture cure) method, making it more rigid than PEX-A, cannot repair kinks—damaged sections must be replaced
PEX-A - compatible with expansion fittings that match pipe diameters, ensuring unrestricted flow. It can also use crimp, clamp, push-fit, or compression fittings
PEX-B - Typically uses insert-style fittings secured with crimp tools. These fittings reduce water flow due to smaller diameters at joints
PEX-A - Superior freeze resistance due to its ability to expand under pressure, making it less prone to bursting in cold climates
PEX-A is more expensive per foot and requires specialized tools for installation (e.g., expansion tools. Ideal for tight spaces requiring sharp bends. Suitable for systems exposed to freezing temperatures
PEX-B - common for standard residential plumbing due to affordability, best suited for areas where flexibility is less critical
Pex Cutter and Crimper
Pex Expander
(expansion tool)
for Pex-A
3/4" Copper Press x PEX Crimp Adapter
3/4" PEX x 3/4" Copper Fitting Adapter (Male Sweat)
Use a crimp tool with copper crimp rings or a clamp tool with stainless steel clamps to secure the PEX side
Comparing, installations
https://www.youtube.com/watch?v=krJrvuaozyc
Pex-B fitting has smaller hole
Pex-A allows using expansion rings:
Slide a PEX expansion ring onto the tube end, insert the expansion tool and expand it , rotate to avoid ridges inside the tubing. The number of expansions: 6 for 1/2-inch, 8 for ¾-inch
Quickly insert the expansion connector into the expanded tubing and hold in place while the tubing contracts around.
A
B

## Slide 22
SharkBite fittings are push-to-connect plumbing fittings
that offer a quick and easy way to connect pipes,
designed for use with water lines and other plumbing applications,
but not gas or air.
Sharkbite Fittings

## Slide 23
Hose Bibb Faucet
a sillcock
boiler drain valve
1/2" MIPS (Male Iron Pipe Size)
Outlet Connection (where a hose attaches): This has 3/4" Garden Hose Threads (GHT). This is the standard size for garden hoses in North America. The threads are coarse and straight (non-tapered).
Inlet Connection (where it connects to the pipe): This appears to have Male National Pipe Tapered (NPT) threads – size 1 / 2 ".
Hose Bibb
1/2 in. x 12 in. Brass MPT x SWT Heavy-Duty Frost Free Anti-Siphon Outdoor Wall Hydrant
IPS = Iron Pipe Size
MIPS = Male Iron Pipe Size
FIPS = Female Iron Pipe Size
NPT = National Pipe Taper
MPT = Male Pipe Thread
FPT = Female Pipe Thread
SWT = Sweat connection = soldering connection (copper)
MPT x SWT: This indicates a dual/universal inlet connection. You have the option to either screw the male threads into a 1/2" female threaded fitting (like FPT or FIPS) OR solder it directly onto a 1/2" copper pipe.

## Slide 24
Pressure Vacuum Breaker
https://www.youtube.com/watch?v=IdASRPrJKq8
check valve & inlet valve
https://www.amazon.com/dp/B00KI0WORE/
Pressure Vacuum Breaker
Check Valve backflow preventer
https://www.amazon.com/dp/B00GZ3H2EI
We need two valves:
Check Valves: Preventing Backflow back into the well. One valve is usually installed in the pump tube, another – just before pressure tank.
Air Release Valve: Preventing Air in the System, reducing noise and preventing air locks. As the trapped air naturally raises up, the valve is usually installed at the highest point in your plumbing system, often near the water heater or at the highest accessible point in the main supply line, definitely above the Pressure Tank.
Air Release Valve (bleeder)
https://www.amazon.com/dp/B07V8TMX95

## Slide 25
Water Testing
https://www.sullivancountylabs.com/
AG ENVIRONMENTAL RSC LLC ( DBA SULLIVAN COUNTY LABS )
86 Queen Mountain Rd, Ferndale, NY 12734
Open M-F 9-5; tel: (845) 704-8151
7/6/2022 – spoke with Carmen – she mailed testing bottles: tests: 10 metalls ($179) + bacteria + nitrates: $250 total
We can use plastic 750 ml Coca-Cola bottle
Olympian Water Testing
https://olympianwatertesting.com
https://olympianwatertesting.com/drinking/water-testing
461 Columbus Ave, New York, NY 10024
open 9am-9pm every day (including weekends)
tel: 646-328-3931. or 212-461-3879

## Slide 26
Aqua-Pure Servicing
Recommendations by Cornell Cooperative Extension
http://genesee.cce.cornell.edu/your-home/well-water
==============================
AG Environmental/Sullivan County Labs
.. https://www.sullivancountylabs.com
AG ENVIRONMENTAL RSC LLC
DBA SULLIVAN COUNTY LABS
86 Queen Mountain Rd, Ferndale, NY 12734
(845) 704-8151
==============================
Valley Water Services
https://valley-water.com/contact/
845-887-4770 Kristen
info@valley-water.com
Plumber
DJS Plumbing
http://www.djsph.com
Phone number
(845) 887-6309
The address in contract:
house: 833 County Road 94, Hankins, NY 12741
barn: 829 County Road 94, Hankins, NY 12741
Former Owners:
Vincent A. Shursky :
Susanne M. Shursky : 845-796-8050

## Slide 27
Water Filter under sink
High quality, designed, engineered and assembled in the USA
System built with US MADE super capacity filters (long lasting for tap/well water)
Effectively remove chemicals (i.e. chlorine), taste and odors.
NOT designed for TDS removal (TDS = Total Dissolved Solids, mostly inorganic salts)
Feed Water Pressure 20-85 psi
APEC Water Systems WFS-1000
3 Stage Under-Sink Water Filter System
$140
https://www.amazon.com/gp/product/B00TT9I2PS/
Installed July 2022
Filters last 1 year
Three filters:
Stage1: 1-SED10 - 5 micron polypropylene filter
Stage2: 23-CAB10 - 10" Extruded Carbon Block Filter
Stage3: 23-CAB10 - 10" Extruded Carbon Block Filter
APEC ULTIMATE Series US Made 2 Sets of Stage 1, 2 & 3 Replacement Filter For Undersink System (FILTER-SETX2)
$80
https://www.amazon.com/dp/B00SSAKT46

## Slide 28
Pipe and washer sizes
Shower: standard 1/2 inch pipe size.
North America (NPT = National Pipe Thread)
British Standard Pipe (BSP) - used throughout Europe, Australia, New Zealand, Asia, South Africa, etc.
Exceptions – some luxury items or very old installations
Standard washer may be made of rubber or silicone.
Standard washer size:
3/4-Inch outer diameter (=6/8 = 12/16)
3/8-Inch inner diameter ( = 6/16)
1/8-inch thickness (3mm)
Alternative I've seen:
11/16-inch outer diameter
9/16-inch inner diameter
Garden Hose: 3/4 inch pipe size.
Buy Heavy Duty Rubber Washer to fit Standard 3/4" Garden Hose Fittings
Typical size:
outer diameter : 1-Inch
inner diameter : 13-18 mm ( 0.51-inch - 5/8-inch)
thickness: 3mm (1/8-inch)