## Slide 1
Wood Stove
Rocket Stove
Masonry Heater
https://tempcast.com
counter-flow design
(hot air goes up, then down the sides, then back – and into chimney
Wood Burning Stove
Russian Stove
Rocket Mass Heater
Rocket Stove

## Slide 2
Peter van den Berg
Peter van den Berg - batch rocket feeding into a bell chamber
"batch rocket design feeding into a bell chamber" - hybrid solution combining batch rocket with Kuznetsov's bell system.
https://batchrocket.eu
https://batchrocket.eu/en/designs – designs
https://www.rocketstoves.com/case-studies/peter-van-den-berg/
https://www.youtube.com/@batchrocketproject4720
https://www.youtube.com/watch?v=VL7O8qLXz24
https://permies.com/t/156820/Experience-Kuznetsov-Stoves
https://roquetinho.eu/files/roquetinho-en.pdf – Roquetinho
https://www.handprintpress.com/tech/improving-woodstove-efficiency-rocket-stoves-masonry-heaters/
https://donkey32.proboards.com/thread/40/rocket-bell-stove – Rocket-Bell
http://www.bergkachel.nl
RMH = Rocket Mass Heater: 90% clean burning, long heat output
Rocket Combustion Core - uses a J-tube or L-tube design where wood burns vertically in a tube. Air enters from below, creating an intense, oxygen-rich burn. The combustion chamber is heavily insulated to maintain very high temperatures (1800°F+). This creates complete combustion with almost no smoke or emissions. It is called "rocket" because of noisy roaring sound
Mass Storage System - made of cob, adobe, brick, or stone (bench seating, sleeping platform, ...). Mass radiates heat for 12-24 hrs after fire dies out
Batch rocket - Load, light, walk away, enjoy heat for 12-24hrs
Hybrid solution: batch rocket feeding into a bell chamber. Hot gases from rocket exit into a bell-shaped chamber (like Kuznetsov's design). The bell acts as a heat trap using natural gas physics. Hot gases rise and swirl in the bell, giving up their heat. Cooled gases naturally sink and exit through a lower outlet. This hybrid solution is simpler than Kuznetsov stoves, proven performance, perfect for a DIY project
Peter van den Berg lives on the west coast of The Netherlands.
He is a retired boat repairman, spending most of his time experimenting with masonry - and Rocket Stoves.
He has been very active in the online discussions about Rocket Mass Heaters, bringing practicality, experience, and science.

## Slide 3
https://en.wikipedia.org/wiki/Rocket_stove
Rocket Stove
A rocket stove is an efficient and hot burning wood stove
Stove has an insulated hot vertical chimney (a "raiser") , where hot gases go up creating strong draft (pull) of gases through the system. It also ensures almost complete combustion
Rocket stoves most often used as portable stoves for cooking
Rocket stoves are also used for heating (rocket mass heaters)
In field tests in India, rocket stoves used 18.. 35% less fuel, compared to the traditional stoves
An Argand lamp (patented in 1780) was a precursor to the rocket stove. Its secret is simply a glass cylinder above the flame to increase air-flow. Same design was used for cooking and heating as it provides strongest heat without smoke.
Larry Winiarski (Aprovecho non-profit) began developing the rocket stove for developing countries in 1980 based on a VITA stove, designed by Sam Baldwin. A stove was designed to make tortillas and won an Ashden Award in 2005. Aprovecho won the same award in 2006 for their rocket stoves. Aprovecho rocket stoves were sold in Lesotho, Malawi, Uganda, Mozambique, Tanzania, and Zambia.
Argand lamp (1780)
https://en.wikipedia.org/wiki/Ami_Argand
Aprovecho Research https://www.youtube.com/watch?v=SUHCsZHNMmg
VITA Stove (early 1980s)
Rocket Stove
(uses heat insulation)

## Slide 4
Rocket Stove – continued, Mass Heaters
http://my.waldenlabs.com/catalog/rocket-mass-heaters/ - resources
https://commonsensehome.com/rocket-mass-heaters/
https://richsoil.com/rocket-stove-mass-heater.jsp
https://www.youtube.com/watch?v=Sqznv5GDSWc
Book: Rocket Mass Heaters, 3rd Ed.
2014 by Ianto Evans, Leslie Jackson
Book: The Rocket Mass Heater Builder's Guide
2016 by E.Wisner & E.Wisner

## Slide 5
Honey Do Carpenter (Darwin Arnold)
Air Crete Rocket Mass Heater (improved)
https://www.etsy.com/shop/HoneyDoCarpenterShop
https://www.youtube.com/watch?v=eC3MITjo8M4&list=PLHsjz15Szmf3_7p4trNDtZGB15jIiW8Ko
https://www.kickstarter.com/projects/86171610/light-and-portable-rocket-mass-heater-design
Super Efficient Homemade Stove
Air Crete (Aerated Concrete)
a foam of cement + foaming agent (oil control hair shampoo)
https://www.youtube.com/watch?v=aSLJCPR1Prw
https://www.youtube.com/watch?v=DGhgFLruyaE
The chimney pipe is heat-insulated, which creates strong draft and full combustion
Darwin Arnold & Melanie

## Slide 6
https://www.youtube.com/watch?v=vXHmcKWfFw4
Stratification Chamber in a Rocket Mass Heater
Hot air goes up,
cold air goes down
To understand how things work,
it helps to think about water going down
(similar to how hot air goes up).
Think about water, how you "prime the pump" by filling tubes with water,
then turn the diagram upside down,
and you will understand how hot air will behave.
.. https://www.youtube.com/watch?v=xOe_xSTqn1k
.. https://www.youtube.com/watch?v=452OyvGdzP4
Hot air goes up, cold air goes down
Hot air goes up, cold air goes down

## Slide 7
Russian Wood Stove

## Slide 8
Masonry Heaters

## Slide 9
Kuznetsovs stove
93% efficiency
no smoke https://www.youtube.com/watch?v=gaXyWyDm2mk

## Slide 10
Buying and Using a Wood Stove

## Slide 11
Wood Burning Stove (Hearth)
Our property ~3K sqft (2K livable+1K basement). Suitable model at Home Depot: Ashley Hearth 3200 (number "3200" means "area 32000 sqft")
It is very good, has window to look at fire, big (22" logs)
Ashley Hearth 3200 model AW3200E-P
(same as US Stove model US3200E-P)
$2,450 at Home Depot (+200 tax, +100 delivery, +2,000 install = $4,750 total) Heating Area: 3,200 sq. ft.
BTU: 152,000
Weight: 400 pounds
Max Log Length: 22 inches Non-catalytic
https://www.homedepot.com/p/Ashley-Hearth-Products-3-200-sq-ft-EPA-Certified-Pedestal-Wood-Burning-Stove-with-Blower-AW3200E-P/313742319
In Canada they like another brand - "DROLET": .. https://www.drolet.ca/en/products/stoves/
Other examples: .. https://www.popularmechanics.com/home/g37791189/best-wood-stoves/
Many stores, for example: .. https://myfireplaceproducts.com/us_en/ht-3000-wood-stove-db07300
Installation cost typically $1,000 - $3000 (depends on how much ventilation work is needed) .. https://homeguide.com/costs/wood-stove-installation-cost .. https://www.houzz.com/cost/70-wood-stove-installation-cost
Hearth: (pronounced (/hɑːrθ/) like in "Heart")
: fireplace
: the floor of a fireplace, the lowest section of a furnace
: Очаг (in Russian)

## Slide 12
Ashley Hearth Products:
https://www.usstove.com/brand/ashley-hearth-products/
https://www.usstove.com/stoves/wood-stoves/
U. S. Stove Co (since 1869)
U.S. Stove acquired:
1994: Clayton Manufacturing
1996: Jensen Manufacturing
1998: Ashley division of Martin Industries
2012: Vogelzang International
So you can see basically the same stove being sold as Vogelzang or as Ashley Hearth

## Slide 13
.. https://www.youtube.com/watch?v=IqJehn5mb9k
Vermont Castings wood stoves

## Slide 14
HearthStone Wood Stoves
https://www.hearthstonestoves.com/wood/wood-stoves/
Good Video:
https://www.youtube.com/watch?v=Sj8rDK4PXxM
Bari Plus
Model: 8172
German made
TruHybrid™ = burns cleanly and efficiently using primary, secondary, and tertiary combustion
Deep Firebox (up to 21½” wide by 20½” deep)
Soapstone HeatLife - over 230lbs of soapstone are used to construct the Mansfield model to offer you plenty of long-lasting comfortable heat (assembled in Vermont).

## Slide 15
"3 ways I improved wood stove heating"
https://www.youtube.com/watch?v=iGZWx0gwRCo
Melted wax stores heat
better than sand or bricks
Passive chimney heat reclaimer
(cooling exhaust, tube-inside-tube)
1) insulated smaller burn chamber
(1/2 size of firebox)
2) Passive chimney heat reclaimer
3) adding thermo storage, (still need more of that)
- https://youtu.be/5-2NuTN_Yzs
- https://youtu.be/qg_s9IzF8sw
- https://youtu.be/hopXmMXrqAY
Wax

## Slide 16
https://www.youtube.com/watch?v=Df-sVM-hxrE
Five Best Wood Burning Stoves
#1 - Vermont Casting - Cast iron, Beautiful color finishes, Top load.
#2 - Hearthstone - Catalytic Combustor - Soap Stone & Cast Iron, Longest burn time, most efficient, side load, rear vent.
#3 - Iron Strike 230 (originally "Country Stove") - Re-Burn System, Steel, Customizable, Different sizes, Blower attachment.
#4 - MF Fire Nova 2 - Catalytic Combustor - Insert & Freestanding, Nice burn.
#5 - Napoleon S Series - Re-Burn System – Steel - Strong brand name, Large viewing window, Shelf compartment.

## Slide 17
- https://www.youtube.com/watch?v=yPtVhpHXg0E
Cast Iron Vs Steel Wood Burning stoves
Cast Iron Stoves .. Pros : More ornate, more colorful, traditional look, retains more heat .. Cons : Not Seamless, More Expensive
Steel Stove .. Pros : Clean & modern look, Cost effective, Seamless, Heats larger area .. Cons : Not as hot, Possibility of warping (because of overheating)

## Slide 18
Catalytic Wood Stove
- https://www.youtube.com/watch?v=_DajfQQN7qM
A catalytic combustor = metal grid with special catalytic coating
that helps to re-burn the gasses and particulates.
It increases efficiency, fewer emissions, longer burn times (30+ hrs)
Secondary burn works by burning off the initial smoke produced from the fire that otherwise would have gone up the chimney.
You will often see a series of holes towards the top rear of the stove above the fire box that forces fresh oxygen over the chamber, reigniting this smoke.
Secondary Burn

## Slide 19
Tips on Using Wood Burning Stoves
Stove Fans using Peltier effect: .. https://www.youtube.com/watch?v=Zd-93HLnkb4
Directing the heat from the stove from basement to a living room upstairs https://www.youtube.com/watch?v=qZxJYOP13ME
Tips: https://www.youtube.com/watch?v=6uuhrdmfnqo
Use insulated tube from outside into the burning chamber to deliver air (to retain heated air inside the room)
Use tube with fan to suck hot air from around the stove to another room
Use Fans to circulate air
Store heat in bricks, sand, or wax
Increase draft (clean chimney, chimney fan)
Use seasoned wood

## Slide 20
Cold Air Intake
Problem:
Stove takes air from inside the room. The air pressure in the room goes down, and this causes a draft of cold air from doors, windows, and ventilation outlets into the room. This draft is cold - thus it reduces the effectiveness of the stove in warming the room.
Solution:
Construct an insulated pipe to deliver the air from outside directly into the bottom of the burning chamber of the stove.
This reduces the draft and improves te efficiency of the stove.
The pipe can be passive – or you can install a fan in the outer end to suck air into the pipe.
A home’s wood stove needs to breathe from somewhere

## Slide 21
How to Run an Overnight Burn
https://www.youtube.com/watch?v=5oledpf2ocU
When starting, use dry paper and kindling to burn through the cold air plug.
Keep door open to get more air.
Fill stove with wood
Regulate air intake
Regulate chimney damper
How to start a wood stove
without it smoking?
https://www.youtube.com/watch?v=hmTkL5oUCDU

## Slide 22
Portable Stove
SilverFire Survival Stove – best Rocket Stove SilverFire® Survivor 2nd Generation rocket stove .. https://www.silverfire.us/survivor-rocket-stove-p10 .. https://www.youtube.com/watch?v=oDGGlaVFqZU (2020) .. https://www.youtube.com/watch?v=IfBKBvTFgXo (2018) .. https://www.youtube.com/watch?v=ujsfXvWAd48 (2018) .. https://www.youtube.com/watch?v=8DwT-Vqy_Uc (2013)
Petromax Rocket Stove rf33 https://www.petromax.de/en/px-produkte/rocketstove-rf33/
SilverFire Scout Stove lightweight wood fired gasifier stove, that operates on just on twigs or flammable biomass
https://www.silverfire.us/304-stainless-steel-scout-stove

## Slide 23
Commercial Pizza Ovens (electric & gas)
Commercial Pizza Ovens

## Slide 24
Kerosene Lamp / Lantern
Dead-flame (1850)
"removing flickering by protecting from side winds"
Hot-Blast (1869)
"the wind supports the flame instead of extinguishing it"
Cold-blast (1873)
"only fresh air is supplied to the burner, thereby increasing the brightness and stability of the flame"
2023 –$10 at amazon
https://www.amazon.com/dp/B000MKOWRU/

## Slide 25
Protect Hardwood Floor Near Fireplace
Stray ember or spark can fly and damage the floor
Use a Screen or Cover
Extend the Hearth
Use a hearth in front of the fireplace (bricks, tiles, stones)
Hearth Pad or Fireplace Rug (fire-retardant) - lay it in front of fire
https://www.amazon.com/dp/B0BL29DRZT/
https://www.amazon.com/dp/B08FTJDK11/
Rug
Screen
https://www.amazon.com/dp/B015NRQ6OS/
https://www.amazon.com/dp/B015NRQA7G/
https://www.amazon.com/dp/B07SHJ1RLN/
https://www.amazon.com/dp/B09WQT32B2/

## Slide 26
Wiseway Pellet Stoves
https://www.youtube.com/watch?v=Kjyf4dBViic
https://www.wisewaypelletstove.com/specs/
https://www.wisewaypelletstove.com/
Natural gravity pellet feed lasts 24-36 hours
Silent
Weight 131 lbs
H x W x D x 52″ x 24″ x 15″
Price ~ $1,500
Can work non-stop for months
Easy to clean
5mm Ceramic glass
Efficiency Rating 75%
Heating Area 2,000 Square Feet
High Temp Burn: 10 hrs, 5.5 Lbs fuel/hr
Low Temp Burn: 30 hrs, 2 lbs fuel/hr
Heat Output 40,000 BTU
Certified and approved for use