## Slide 1
Electric Work
Twist Wire Connectors
(a.k.a. marettes, wing nuts, wire caps, wire twists)
https://www.youtube.com/watch?v=9hlo87E_GdQ
https://www.thespruce.com/electrical-code-for-outlets-1821513
circuit breaker
electrical panel
Maximum current in cables (in Amperes):
gauge\len 50ft 100ft 150ft
16 1-13 1-10
14 white 14-15 11-13 1-7
12 yellow 16-20 14-15 8-10
10 orange 16-20 16-20 11-15
8 black up to 40
6 up to 55
Cable types:
NM-cable = Non-metallic (a.k.a Romex cable):
AC-cable = Armored Cable (a.k.a. BX cable) – flexible metallic sheathing.
UF-cable = Underground Feeder Cable – outdoors, underground. Non-metalic, solid plastic sheathing, gray color.
Metal-Clad Cable - running through unfinished areas like basements.
Wires inside cables:
- one hot (black or red)
- one neutral (white)
- one bare ground
outlet
Toggle Light Switch
WAGO Lever-Nuts
Knot wires together
Wire Strippers
screw colors:
brass – hot,
silver – neutral,
green - ground
GFCI = Ground Fault Circuit Interrupter

## Slide 2
Push-in wiring, sometimes branded "QuickWire", uses holes in the plastic casing, underneath which are sharp spring-loaded cleats that catch and hold the wire when you put it in. It compresses on the wire more when the side screw is tightened.
Most electrician I know uses the back connections on GFI's and side wires regular receptacles.
When inserting the wire, release the screw and tip the device so the grab plates would open.
To remove them, you take a jeweler's screwdriver or a small pick or probe and push into a square tab nearby, which pushes the cleat away allowing you to withdraw the wire.
Many people hate "push-in" because:
.. they are designed to work only with one gauge of wire (either 12 or 14AWG depending on the type of switch or outlet).
.. getting the wire out of the hole without damaging it is difficult
It is safer to use the side-clamping. Make sure to add isolation tape to prevent shorting on metal parts of bare ground.
"Push-in" QuickWire terminals